## Slide 1: Circuits!

## Slide 2: ELECTRical & Computer Engineering
It all starts with the electron
Electrical current, charge, fields, magnetics, power, …
Electron?
  Elementary particle, carries a negative charge
Holes?
  The absence of an electron where one could exist
Will move from point A to B given a voltage

## Slide 3: Electrons
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Current
e-
h+
e-
h+
e-
h+
e-
h+
e-
h+
e-
h+
e-
h+
e-
h+
e-
h+
e-
h+
+
-
Voltage

## Slide 4: ECE Fundamentals
Fundamentals of ECE:
  Resistors (R), capacitors (C), inductors (L)
  Battery, Voltage Supply, Ground
  Current (I)
    Flow of electric charge
    Note: current is the movement from + to -
  Voltage (V)
    Electric potential between 2 points
Component
+
-
v
i

## Slide 5: Simple Circuit
Ohm’s Law: V = IR or I = V/R or R = V/I
+
-
5V
5 kΩ
1 mA
V
I
I-V characteristic curve of a resistor

## Slide 6: Water, Water Everywhere
Water makes a good analog for the world of electricity
Voltage (potential difference)  Water pressure
Current (flow of charge)  Flow of water
Wire  Pipe
Water examples from: “Electrical Engineering Uncovered,” D. White & R. Doering

## Slide 7: Pipe Width
Given the same water pressure, which pipe’s water is moving faster
Water per second is proportional to area
Electrical is the same way, larger wires have less resistance, and higher current (given the same voltage)
Another analogy: traffic: more lanes = less resistance

## Slide 8: Resistor
To build a resistor, vary length, material, and area to change the voltage/current characteristics
What if I put a sponge in the constricted part?
Given the amount of water passes through, which has the higher pressure?
The pressure (voltage is proportional to the resistance)
  Voltage = Resistance * Current
Ω

## Slide 9: Electronic Color Codes
Resistors (and other components) have color bands to identify
First 2 bands are digits of the value, 3rd is the multiplier
  Green-Blue-Red
  5 6 102 = 5600 = 5.6 kOhms
Mnemonic
Black Brown Red Orange Yellow Green Blue Violet Grey White
Better Be Right Or Your Great Big Venture Goes Waa
- waa
0 1 2 3 4 5 6 7 8 9

## Slide 10: Tolerance
The last stripe is tolerance
or variation
Electrical components come
with some variability
Resistors, capacitors, motors, transistors, etc…
5.6kOhm transistor with 10% variability
  Possible range from 5.04kOhms to 6.16kOhm

## Slide 11: Series/Parallel
In series, resistors see the same water flow (current), but different individual pressures (voltage)
In parallel, the resistors see the same pressures (voltage) at either end, but different current flow (current)

## Slide 12: DC Voltage/Current Sources
Provide the energy to move the water
  Motor/pump
  Gravity (water tower)
+
-
-
+
+
-

## Slide 13: Water Flow Potential
Potential

## Slide 14: Capacitor
Water/electricity pushes the piston and pushes out water (no extra water passes the piston)
When the source disconnects, capacity is pushed out/unloaded
As springs coil, more energy needed to push them closed
  When released, quick at first, then slows down

## Slide 15: Capacitor Details
+ + + + + +
2 parallel plates separated by a dielectric material
Capacitance is a result of the dielectric material, the area of the plates, and the distance between the plates
+ + + + + +
- -
- - -
filled with dielectric
C = A/d

## Slide 16: Capacitance
Measured in Farads
Capacitance = Charge/Voltage
  C = Q/V  Q = C*V  dQ/dt = C*dV/dt
Current through a capacitor = Capacitance * Change in voltage
  i = C*dv/dt
  Voltage across a capacitor cannot change instaneously

## Slide 17: Water Flow (Capacitor)
Potential

## Slide 18: Water Flow Time Lapse

## Slide 19: Inductor
Current pumps in, gradually increasing, and once it gets going, takes time to stop
  Releases its energy

## Slide 20: Inductor Details
Wires wrapped/coiled around a core
As current passes through, magnetic charge is stored
  When disconnected, it will push current and lose energy

## Slide 21: Inductance
Measured in Henrys
Voltage across an inductor = Inductance * Change in current
  v = L*di/dt
  Current through and inductor cannot change instaneously

## Slide 22: LC Oscillator
Once charged, will send the energy back and forth
  If you monitor the movement at the top
Frequency (in radians) = 1/√(L*C)

## Slide 23: C vs. L
Capacitor stores energy in an electric field
Inductor stores energy in magnetic field
Capacitor’s voltage cannot change instantaneously
Inductor’s current cannot change instantaneously
Capacitors become an open circuit at DC and short circuit at high frequency
Inductors become a short circuit at DC and an open circuit at high frequency

## Slide 24: Diode
Diode allows current flow in 1 direction

## Slide 25: BJT
Bipolar Junction Transistor
base
collector
emitter
base
emitter
collector

## Slide 26: MOSFET
PMOS vs. NMOS
For PMOS
  if gate is ‘1’, no current flow
  if gate is ‘0’, current flows
  from source to drain
Negative
pressure
Gate
Source
Drain
Gate
Source
Drain
Gate
Source
Drain
Positive
pressure
Gate
Source
Drain
For NMOS
  if gate is ‘0’, no current flow
  if gate is ‘1’, current flows
  from source to drain

## Slide 27: There are more analogies
Transformers, AC sources (low and high frequency), potentiometer,
Flow of water  flow of electrical charge (electrons/holes)
You will see plenty of electrical circuits
  Kirchoff’s laws, Ohm’s law, mesh/node analysis

## Slide 28: Summary of Electrical Quantities
Quantity | Unit | Important Equations
Charge (Q) | coulomb (C) | i = dq/dt
Current (I) | ampere (A) | 
Voltage (V) | volt (V) | 
Power (P) | watt (W) | P = dU/dt P = I*V
Energy (U) | joule (J) | U = Q*V
Resistance (R) | ohm (Ω) | V = IR P = V2/R = I2*R
Capacitance (C) | farad (F) | Q = CV U = ½*C*V2 i = C*dv/dt
Inductance (L) | henry (H) | U = ½*L*I2 v = L*di/dt

## Slide 29: AC vs. DC
You’ve seen both
DC = battery, solar cell, fuel cell
  No changes to current/voltage level
AC = turbine
  Spinning rotor passes magnets to produce current
  Current/voltage alternates between min and max in a sinusoid

## Slide 30: Generator
Turn a loop of wire inside of a magnet
  The change in magnetic field creates a current (thank you, Faraday)http://www.generatorguide.net/howgeneratorworks.html
I

## Slide 31: Edison vs. Tesla
War of the Currents
  Edison (DC) vs. Tesla/Westinghouse (AC)
Edison used to burn/electrocute cats saying that AC power was responsible
  Called it being “Westinghoused”
  Led to the first electric chair (by accident)
AC current is easier to distribute thanks to transformers (high voltage, low current)
http://theoatmeal.com/comics/tesla

## Slide 32: Measurements
Aside from component values
  Resistor (Ohm); Capacitor (Farad); Inductors (Henry);
Voltage: Amount of electric potential
Current: Charge per time
Energy: Amount of work to produce voltage/current in order to move the charge
Power: Amount of energy per unit time

## Slide 33: With what to measure
Oscilloscope: Measures across time
Multimeter: Instant reading
  Voltmeter/Ammeter

## Slide 34: How to measure
To measure current:
  Must be in the path
To measure voltage:
  Must be outside the path
To measure power/energy:
  Record the current/voltage/component characteristics
  Do the math

## Slide 35: Simple Circuit
Ammeter – Measures current through a point
  If you measure across a component, all the current will go around the component, changing circuit behavior
Voltmeter – Measures voltage across a component or many
  If you measure voltage across no component, it has no resistance, which means there is no difference
+
-
5V
5 kΩ
1 mA
V
A

## Slide 36: Power and Energy
Power = I * V
= I * (IR) = I2R
= V/R * V = V2/R
Energy = Power * Time
Power and energy are often interchanged
  Power is often how much heat is produced
  Energy is how quickly your battery drains

## Slide 37: Breadboard

## Slide 38: CAD/Circuit Software

## Slide 39: Soldering